## Slide 1
Environmental Impact Assessment for
Armenia's Proposed Nuclear Power Plant
Presented by:
Lief Erickson
DCOP of USAID Energy Security and Regional Integration Project
Yerevan, November 08, 2012
In cooperation with
Aram Gevorgyan, Head
Atomic Energy Department, RoA Ministry of Energy and Natural Resources

## Slide 2: Who Am I?
International Experience
International Nuclear Safety from1997-2001
  Quality Assurance
  Event Analysis Reporting and Lessons Learned
  Startup of Nuclear Power Plant Operational Support Institute
Licensing Consultant for Chornobyl Shelter since 2001
  Assistance to the nuclear regulatory authority of Ukraine in review of Chornobyl Shelter Projects
Assistance to the Energy Sector of Armenia since 2007
  Lead Author of the Environmental Background Information Document for the new nuclear project in Armenia
  Contributor to the Initial Planning Study for the new nuclear project
  Deputy Chief of Party of the Energy Security and Regional Integration (ESRI) project
  Assistance to the Ministry of Energy and Natural Resources in collection and organization of data for the Armenia New Nuclear Unit Environmental Report

## Slide 3: USAID Energy Security and Regional Integration Project
The ESRI “New Nuclear Plant Development” task is to provide independent expert services to support the GoA in: assuring that the new nuclear unit meets international safety and environmental standards; in enhancing the human and institutional capacity to implement the project; and in maximizing the contribution of the project to Armenia’s economic growth and development
ESRI also has tasks to improve the enabling environment for development of renewable energy in Armenia and to support Armenia’s integration into regional energy systems and markets

## Slide 4: Armenia New Nuclear Unit (ANNU) – Project Milestones
  1 November 2007 – GoA Resolution № 1296 adopted the 2006 Least Cost Generation Plan (LCGP) as consistent with its energy strategy
    The 2006 LCGP concluded that a new nuclear unit was least cost option for replacement of Armenia Nuclear Power Plant Unit 2 when it reaches the end of its design life in 2016
  October 27, 2009 – RoA Law “On Construction of New Nuclear Energy Unit(s) in the Republic of Armenia” directed development of new nuclear unit(s) with total capacity up to 1200 MW
  December 2009 – CJSC “METSAMORENERGOATOM” established to function as developer of the ANNU
  July 26, 2010 – Notification to the Ministry of Nature Protection under the Law on EIA
  August 24, 2010 – Public hearing on the notification held in Armavir Marzpetaran
  August 27, 2010 – Notification sent to the Secretary of the Espoo Convention
  September 1, 2010 – Notification sent by Espoo Secretary to representatives of Azerbaijan, Georgia, Turkey, and the Islamic Republic of Iran

## Slide 5: ANNU Project Milestones - continued
  March 21, 2011 – ANNU Environmental Report (Rev. 0) submitted to the Ministry of Nature Protection
  May 17, 2011 – Public Hearing in Armavir Marz
  May 24, 2011 – Public Hearing in Gyumri, Shirak Marz
  July 21, 2011, August 3, 2011 and August 19, 2011 – Comments and opinions on the ANNU ER provided by Environmental Expertise SNCO
  September 14, 2011 – Responses to comments and opinions submitted to Environmental Expertise SNCO
  December 20, 2011 – Head of Staff of the Ministry of Nature Protection provided a letter summarizing the Ministry of Nature Protection’s consideration of the ANNU ER with attached objections from a professional conclusion
  November 2012 – The Ministry of Energy and Natural Resources posts on their website Revision 1 of the ANNU ER (http://www.minenergy.am/en/en/atomhashvetvut) documenting: transcripts of the public hearings and responses to issues raised; responses to issues identified by the Ministry of Nature Protection; updates of environmental data related to water uses; and a summary of the Seismic Hazard Analysis for the ANNU site.

## Slide 6: Environmental Impact Assessment in Armenia
RoA Law on Environmental Impact Assessment (EIA), November 1995
  Nuclear power facilities require an EIA
  Notification is submitted to the Ministry of Nature Protection and Public of project requiring EIA
  First Public Hearing on the Notification of intent to build project
  Submittal of environmental documentation by the Developer to the Ministry of Nature Protection
  Second Public Hearing on the environmental documentation
  Ministry of Nature Protection organizes Expertise review of environmental documentation and receives Expertise Conclusion from experts
  Third Public Hearing on the Expertise Conclusion
  Ministry of Nature Protection makes decision on the issuance of assessment conclusion (EIA) and issues conclusion to developer and the GoA
  The Government of Armenia approves the EIA

## Slide 7: Internat’l Conventions and Standards Applicable to EIA
  United Nations Economic Commission for Europe (UNECE) Convention on Environmental Impact Assessment in a Transboundary Context (Espoo, 1991)
    Establishes an EIA procedure that provides for notification of concerned parties and public participation and consultation of affected parties
    Armenia and Azerbaijan are parties to Espoo
  UNECE Convention on Access to Information, Public Participation in Decision-making and Access to Justice in Environmental Matters (Aarhus, 1998) – Armenia, Georgia and Azerbaijan are parties
  Convention on Nuclear Safety, (Vienna, 1994) – Armenia is a party
  IAEA Safety Requirements, Standards and Guidelines
  Policies and Procedures of International Financing Organizations:
    Export Import Banks of the US, Canada, and the EU
    World Bank
    European Bank for Reconstruction and Development (EBRD)
    Asian Development Bank

## Slide 8: Information Needed for EIA of Large Power Project
  Information on the existing environment at the Project location – ESRI collected information with the assistance of the Ministry of Energy and Natural Resources and information available from public sources – libraries and Internet:
    Meteorology and Air Quality
    Land Use and Socio-economic conditions in the Project location, vicinity and region
    Water availability to serve Project needs
    Ecological Conditions in the Project location and vicinity
    Geology of the Project site and vicinity
  Description of the Project – ESRI relied on information provided by the Ministry of Energy and Natural Resources; where key parameters were not defined, ESRI developed bounding plant parameters that should maximize potential environmental impacts relative to possible design decisions
  Environmental Impacts of Project Construction – ESRI tabulated impacts based on information provided by the Ministry of Energy and Natural Resources and on impacts based on generic studies and environmental impact statements developed for NRC licensing of plants in the US

## Slide 9: Information Needed for EIA … (continued)
  Environmental Impact of Project Operation – ESRI tabulated impacts based on information provided by the Ministry of Energy and Natural Resources and generic impacts based on studies and environmental impact statements developed for NRC licensing of plants in the US – bounding plant parameter approach enabled prediction of impacts without final design details
  Environmental Monitoring Programs – ESRI described monitoring programs needed to complete design, to monitor impacts of construction, to establish baselines for impacts of operation, and to monitor impacts of operation
  Impacts of Accidents at the Project Involving Radioactive Materials (topic unique to nuclear projects) – ESRI tabulated impacts based on information provided by the Ministry of Energy and Natural Resources
  Alternatives to the Proposed Action – ESRI summarized alternatives evaluated in the 2006 Least Cost Generation Plan

## Slide 10: Ministry of Nature Protection Position on the ANNU ER
  The Ministry of Nature Protection letter of December 20, 2011 to CJSC “METSAMORENERGOATOM” stated:
  After getting responses to issued raised during the Environmental Expertise , the corresponding authorities and bodies provided in general positive opinions
  Numerous project solutions that may have a potential environmental impact require additional study, some equipment is not chosen yet, and some of the assessments are not final
  At the next stage of the project it is necessary to consider the recommendations, as well as to provide the final technical and technological solutions together with the impact assessments, required measures and their justifications
  The RoA Ministry of Nature Protection does not have any principle objection towards the ANNU ER
  The final expertise conclusion on the ER will be provided upon submission of the final version of the ER to the Ministry of Nature Protection for environmental impact expertise

## Slide 11: Current Status
  The Ministry of Energy, based on recommendations of their consultant Worley Parsons, selected AtomStroyExport model AES-92 VVER-1000 for the ANNU
  The Russian Federation has pledged to fund manufacture and construction of the ANNU “Nuclear Island” – estimated to be up to 20% of project cost
  GoA plans to involve additional investors for the remaining project costs
  It is not possible to have the ANNU operational before expiration of the Armenian Nuclear Power Plant, Unit 2, design life in 2016
  The GoA has decided to extend the lifetime of Unit 2 up to ten years, or until the ANNU is operational
  The Ministry of Energy and Natural Resources has initiated activities to prepare a new Least Cost Generation Plan considering current predictions for electrical demand in Armenia, revised predictions of prices for import of natural gas, electricity import and export potential, and alternatives to replacement of ANPP generation capacity
  If the proposed 1000 MW ANNU is to be built, the ANNU ER must be completed with final design details on the plant and submitted to MoNP

## Slide 12: Moving Forward
  Key Issues
  Water
    Selection of cooling technologies for the ANNU
    Competing water users and water allocations by Water Management Agency
    Improving irrigation technologies
  Radioactive Material Dispersion Predictions
    Representative data on meteorological conditions at the site
    Radioactive source terms for releases during accidents and normal operations
  Transport of Heavy Equipment and Components
    Very large and heavy equipment will require upgrade of transport routes
  Export Potential for excess generation

## Slide 13: QUESTIONS

## Slide 14: THANK YOU FOR THE OPPORTUNITY TO SPEAK TO YOU THIS EVENING